## Slide 1: HG5020-AX15-3G
3GE + USB2.0 + WiFi6
Application Chart:
VSOL product datasheet | Updated: 08-12- 2021 | Rev.2.0 | www.vsolcn.com
ONT
Internet
OLT
Computer
Mobile phone
USB storage device
USB Printer
HG5020-AX15-3G
Key Features:
Next-Gen Gigabit WiFi
Speed up to 1.5 Gbps
Connect More Devices
OFDMA + MU-MIMO
RTL CPU Chipset + Wi-Fi Chipset(2.4GHz With FEM),
High Performance Solution
Introduction:
HG5020-AX15-3G(3GE+USB2.0+WiFi6 AX1500 Wireless Router) adopts WiFi6 technology which has redefined home WiFi. Experience up to 3x faster speeds, higher capacity, and reduced congestion overall compared to the previous AC WiFi5 standard. The AX1500 4-stream dual-band WiFi6 wireless router reaches speeds of up to 1.5 Gbps, for a buffer-free 4K/HD streaming and gaming experience. The WiFi6 router lets you connect even more devices via OFDMA technology, minimizing network congestion that occurs with too many connected devices. Realtek CPU Chipset and Realtek Wi-Fi Chipset effortlessly handle all your streaming, gaming and smart home devices. HG5020-AX15-3G uses Beamforming technology to focus WiFi signal to your devices for more reliable coverage. The HG5020-AX15-3G is easy use and setup with WebUI.
WPA3
More Security

## Slide 2
Product Name | Product Description | Accessories
HG5020-AX15-3G | 3*GE+USB2.0+WiFi6 | AC-DC power adaptor: DC12V/1A
Official Website: https://www.vsolcn.com/ E-mail: sales@ftthcpe.com support@ftthcpe.com
Dimension | 115*115*135mm(L×W×H)
Net weight | 0.350KG
Working condition | Working temp: 0~+50°C Working humidity:5~90%(non-condensing)
Storing condition | Storing temp: -30~+60°C Storing humidity:5~ 90% (non-condensing)
Power adapter | DC 12V/1A
Power supply | ≤10W
Interface | 3*GE + WiFi6 + USB2.0
Indicators | STATUS(1), RJ45(3)
Button | Reset, WPS
Hardware Parameter
User Interface | 3*10/100/1000Mbps auto adaptive Ethernet interface , RJ45 connectors(1*WAN, 2*LAN)
WLAN Interface | Compliant with IEEE802.11b/g/n/ac/ax 1200 Mbps on 5GHz and 300Mbps on 2.4 GHz 2.4Ghz: 2*2, 5GHz: 2*2; 4*4dBi internal antenna Maximum number of connected devices: 32 for 2.4GHz and 32 for 5GHz
USB | 1×USB 2.0 for Shared Storage/Printer
Interface Parameter
WAN | Maximum speed of 1Gbps
Wireless | Wi-Fi 6: 802.11a/n/ac/ax 5GHz & 802.11b/g/n 2.4GHz WiFi Encryption: WPA/WPA2/WPA3 personal, WPS2.0 Support MU-MIMO & OFDMA Support Beamforming Support Beamsteering Support WIFI Easy-mesh function
L3/L4 | Support IPv4, IPv6 and IPv4/IPv6 dual stack Support DHCP/PPPOE/Statics Support Static route,NAT Support DMZ, ALG,UPnP Support Virtual Server Support NTP (Network Time Protocol) Support DNS Client and DNS Proxy
DHCP | Support DHCP Server & DHCP Relay
Security | Support local access control Support IP address filtering Support URL filtering Support Anti-DoS attack function Support Anti-port scanning function Suppression of protocol-specific broadcast/multicast packets (e.g. DHCP, ARP, IGMP, etc.) Support Anti-Intranet ARP Attack Support Parental control function
Function Data
Function Data
Management | WEB/Telnet/TR-069/Cloud Management
Multicast | Support IGMP v1/v2/v3 Support IGMP Proxy an Snooping