## Slide 1: V2124-4G-4S-P
VSOL product datasheet | Updated: 19-11-2021 | Rev.1.3 | www.vsolcn.com
24*GE PoE Ports+4*GE Ethernet Ports+4*GE SFP Ports Managed Switch
Introduction:
VSOL V2124-4G-4S-P series switches adopt high-quality network chips and stable POE chips, which can not only provide high-speed and stable network connection for Internet devices, but also provide power for Internet devices (such as IP cameras, wireless APs, etc.), which is convenient for users. VSOL V2124-4G-4S-P switch is compatible with 1U rack mount.
VSOL V2124-4G-4S-P switch has 24 *10/100/1000Mbps auto-negotiation PoE Ports, 4 *10/100/1000Mbps Combo Ports, 1 * Console Port，can provide seamless connection for 10/100/1000M Ethernet, supports WEB management, conforms to IEEE802.3af/IEEE802.3at PoE protocol, and is highly reliable.The product can be widely used in security network video surveillance, hotel, campus, small and medium-sized enterprise network engineering and other occasions.
Key Features:
Compliant with IEEE802.3at(30W),IEEE802.3af(15.4W)
Support PoE Watchdog
Support AAA authentication,802.1x authentication,TACACS+ authentication
Support QoS data priority
Support SNMP/Telnet/SSHv2/CLI/WEB/RMON
Application Diagram:
IP Camera
IP Phone
Wireless AP
NVR
V2124-4G-4S-P
Data & POE
Data
Fiber optic
Optical Switch
V3500-28X
Internet

## Slide 2
Item |  | V2124-4G-4S-P
Port | Uplink Ethernet port | 4*GE(RJ45, Combo)
 | Uplink optical port | 4*GE(SFP, Combo)
 | PoE port | 24*GE(RJ45, POE)
 | Management port | 1*Console
Product | Dimension (LxWxH) | 440×280×44mm
 | N.W | 3.65kg
Package | Dimension (LxWxH) | 500×365×85mm
 | G.W | 4.36kg
Switching Capacity(Gbps) |  | 56
Packet Forwarding rate(Mpps) |  | 41.66
Packet Buffer Memory(Mbytes) |  | 4
MAC Address |  | 8K
Jumbo Frame |  | 9.6 Kbytes
Transfer Mode |  | Storage & Forward
PoE Protocol |  | IEEE802.3af(15.4W), IEEE802.3at(30W)
Network Medium | 10BASE-T | Cat3, 4, 5 or above UTP/STP(≤100m)
 | 100BASE-TX | Cat5 or above UTP/STP(≤100m)
 | 1000BASE-TX | Cat5 or above UTP/STP(≤100m)
Fiber Medium | Multi-mode Fiber | 50/125、62.5/125、100/140um
 | Single-mode Fiber | 8/125、8.7/125、9/125、10/125um
Power Voltage |  | Input: AC 100~240V/50Hz~60Hz
Whole Machine power |  | ≦400W
Surge Protection |  | General 6KV, ESD 8KV air, 6KV contact
Working Environment | Operating temperature | -10~+50°C
 | Storage temperature | -40~+70°C
 | Operating Humidity | 10~90% (non-condensing)
 | Storage Humidity | 5~90% (non-condensing)
V2124-4G-4S-P
24*GE PoE Ports+4*GE Ethernet Ports+4*GE SFP Ports Managed Switch
Technical Specifications:
O&M
SNMP/Telnet/SSHv2/CLI/WEB/RMON
Firmware Upgrade
Upload and download configuration
Support SNTP
Equipment Diagnosis
Support Syslog
Layer2 Functions
Link Aggregation：
Load Balancing Policy(base on IP/MAC)
Static and Dynamic Group
Max. 8 link Aggregation groups
VLAN range:1~4094, Max. 256 VLANs
Access/Trunk/Hybrid mode and QinQ
VLAN tag/Un-tag ,VLAN transparent transmission
Support Protocol VLAN and GVRP
Support 802.1D and 802.1W protocol
Support STP/RSTP/MSTP
Support LLDP protocol
Support IEEE802.x flow control
Port stability statistic and monitoring
Support Port Mirroring
Security
Storm Control
Port Isolation, Port Rate-limit, Port Security
Loopback Detection
Support ACL
Support AAA authentication，802.1x/RADIUS/TACACS+ authentication
Dynamic ARP Inspection
IP Source Guard
QoS
Traffic classification based, Strict priority and WRR
Port Priority
802.1P/IP TOS/IP DSCP Priority
Supports up to 8 queues per port
Multicast
IGMP V1/V2/V3
IGMP Snooping
MLD Snooping and MVR
IGMP groups filtering and Querier
DHCP
DHCP Server
DHCP Relay(Option 82)
DHCP Snooping
Layer3 Functions
IPv4/IPv6 dual stack
IPv4/IPv6 static routes
IPv6 ND
PoE
PoE Temperature Query
PoE Type/Level/Power/Voltage/Current Query
PoE Watchdog

## Slide 3
Specifications：
Item |  | V2124-4G-4S-P
LED Indicator |  | PWR，SYS，PoE/ACT，Link/ACT
PWR(Power Indicator) | Lighting | Powered
 | Un-Light | No Power
SYS(System Indicator) | Lighting | System Running
 | Flashing | System Start-up
PoE/ACT(PoE Indicator) | Lighting | PoE on
 | Un-Light | PoE off
Link/ACT(Link & Data) | Lighting | Link connection
 | Un-Light | Link disconnect
 | Flashing | Data transmission
Reset |  | Short press restart
 |  | Long press 5 seconds to restore factory Settings